1. Configure all the router interfaces with ip addresses for each interface.
  ip add <ip_address> <subnetmask>
  f0/0: ip add 10.0.0.1 255.0.0.0 (between two routers)
  ip add <gateway_address_network> <subnetmask> (between router and switch)
  e1/1: ip add 192.168.1.30 255.255.255.224
2. IP route to connect each router to all the networks together.
  ip route <destination_network_address><subnetmask><hop_address>
  do wr
  dhcp: ip route 20.0.0.0 255.0.0.0 10.0.0.2
  do wr
  end (once you’ve connected the router to all the networks it doesn’t reach, do it backwards too)
3. Try pinging between the router networks by assigning just one VPCS in each network with an ip address.
  ip <ip address/subnetmask><gateway_address>
  ping <ip_address_of_a_vpcs_in_another_network>
4. To set up VLAN configuration, double click on switch and set trunk port on whichever port number is connected to a switch or router.
  For the other ports connected to VPCS set VLAN id (vlan1 has an id of 10, vlan2 has an id of 20, random numbers).
5. Configure the router to set up VLAN, go to router and configure it with a random ip address first on the interface connected to the VLAN/switch.
  R4: int e1/1
  R4: ip add 60.0.0.0 255.0.0.0
  R4: no shut
  Then configure the VLANs ip addresses.
  R4: int e1/1.1
  R4: encapsulation dot1q 10

ip add <gateway_address_vlan1_after_splitting><subnetmask>
*Note: Subnetmask for two VLANs in the same network is the same.*

R4: ip add 192.168.1.38 255.255.255.248
R4: no shut
R4: int e1/1.2
R4: encapsulation dot1q 20
R4: ip add 192.168.1.46 255.255.255.248
R4: no shut
R4: end
R4: ip routing
R4: do wr
1. To set up DHCP do the following.

DHCP: config t

ip dhcp pool <pool-name>
network <network_address><subnetmask>
default-router <gateway_address>
dns-server <dns_server_ip_add>

DHCP: ip dhcp pool linux-lab
DHCP: network 192.168.1.0 255.255.255.224
DHCP: default-router 192.168.1.30
DHCP: dns-server 40.0.0.2

ip helper-address <dhcp_ip_add>

Note: For each interface in a router connected to a network of VPCS set the ip helper	adddress.

Do it for the sub-interfaces for VLAN too.

Make a pool for the individual VLANs too.

To set up DNS server do the following. Go on the router that you want to configure as the DNS server and do the following.

ip dns server
ip name-server <dns_ip_add>
ip domain-name <domainame.com>
ip host <hostname.domainame.com> <ip_of_host>
R5: config t
R5: ip dns server
R5: ip name-server 40.0.0.2
R5: ip domain-name oslab.com
R5: ip host os1.oslab.com 192.168.1.34